## Slide 1: ECE477 Midterm Design Review: Team 8

## Slide 2: Outline
Project Overview
Major Components
Block Diagram
Packaging Design
Electrical Schematic
PCB Layout
Prototyping Progress
Software Development Status
Project Timeline
Questions

## Slide 3: Project Overview
Sink or Be Sunk is a 21st century take on the classic Battleship game by Hasbro.
Allows users to play at a distance with Wi-Fi enabled boards that communicate with a server.
Incorporate tactile user input similar to the original game.
Includes audio, visual, and haptic feedback.

## Slide 4: PSSCs
An ability to detect when a user positions their ship pieces on the game board.
An ability to provision a Wi-Fi connection through a Bluetooth BLE connection to a user’s smartphone.
An ability to light individual LEDs in a matrix in response to game events.
An ability to relay game move information between players over an internet connection.
An ability to provide physical feedback to a user with a rumble motor when a ship is sunk.

## Slide 5: Major Components
ESP32
  Powerful Computational power
  Has necessary peripherals (GPIO, DAC, SPI)
  Can communicate on BLE and WIFI
  Low-cost
Microcontroller
MCU | Core | WIFI/BLE | DAC | GPIO | Price
ESP32 | Xtensa Dual-Core | Yes | 2 8-bit Channels | 34 | $8.95
ESP32-S2 | Xtensa Single-Core | Yes | 2 8-bit Channels | 43 | $10.73
ESP8266 | Tensilica L106 32-Bit | Yes | None | 17 | $6.95

## Slide 6: Major Components
Worldsemi WS2812C
  Individually soldered LEDs
  Data-in to Data-out line
  Automatically utilizes PWM
  LED strips use these, but take more power and money
LED
LED Type | Control | Power Consumption | Price per board
WS2812C | Daisy-Chained Shift register | 6 W | $12.8
LED Strips | Individually Addressable LEDs | ~15 - 45 W | $20 - $30

## Slide 7: Major Components
Motor – Jinlong JQ24-35F580C - $5.46
  DC Vibration Motor for response to game events
Keypad – Technological Arts 4x4 Matrix Keypad - $8.00
  Utilized from ECE362 for User Coordinate input
  Through Hole Mount
LCD – Orient Display AMC1602AR-B - $12.69
  16x2 Blue LCD character Display Module
  SPI communication for User Experience
Speaker – Soberton SP-4005Y - $1.85
  General Purpose 400 Hz – 5 Khz Speaker
  Plays sounds in response to game events
Motor, Keypad, LCD, Speaker

## Slide 8: Major Components
Boat Detection
  Boats have a 4-pin male connector on tip and tail of boat
  Plugs into a 4-pin female connector that creates a High voltage level
  Software detects boat information on length
Power
  5 Volt USB Charging brick
  Switching Regulator
  Backup LiPo Battery
Boat detection & Power
Notes: power other options:
AC to DC on board
  most industry product don’t do this as it makes for a more bulky package
9V barrel jack
  This wouldn’t allow for USB programming, need an additional usb port

## Slide 9: BAttery POwer Calculations
description | voltage (V) | current (mA) | quantity | power (watt)
ESP32 | 3.3 | 750 | 1 | 2.475
LED RGB | 3.3 | 15 | 128 | 6.336
LCD Screen | 3.3 | 250 | 1 | 0.825
Speaker | 0 | 0 | 1 | 1.000
Resistive Ships | 3.3 | 0.00033 | 10 | 0.000
 |  | 1015.00033 | Total | 10.636
 |  | 790.712 | Total RSS | 6.925
Battery (Min) | 3.7 | 2600 | 1 | 9.62
 |  | hrs-> | Play Time (Min) | 0.90
 |  |  | Play Time (Typ) | 1.39

## Slide 10: Block Diagram
Microcontroller
ESP32
Speaker
LCD
Button Matrix
4x4
Rumble Motor
Ship Slot 0
8x1
Mux0
8x1
Mux7
8x1
Mux
LED Daisy Chain 1
LED Daisy Chain 128
…
Backup
Battery
DCDC Converter
Ship Slot 63
…
8
8
8
1
1
SPI
(no MISO)
3
8
3
3
…
USB
USB to UART
Charger
2
4
2
1
1
2
2
Legend
3.3 Volts
5 Volts
2
Game Server
User
Device
DAC

## Slide 11: Packaging Design
External Dimensions
33.5cm x 27.0cm x 8.0 cm
Internal Dimensions
32.7cm x 20.5cm x 3.9cm

## Slide 12: Packaging Design

## Slide 13: Packaging Design
Boat Design

## Slide 14: Electrical Schematic – Grid pcb
Overview

## Slide 15: Electrical Schematic – Grid pcb
Connectors

## Slide 16: Electrical Schematic – Grid pcb
input selection mux

## Slide 17: Electrical Schematic – Grid pcb
Input/LED Nodes

## Slide 18: Electrical Schematic – Grid pcb
LED/Input node

## Slide 19: Electrical Schematic – ESP pcb
Overview

## Slide 20: Electrical Schematic – ESP pcb
ESP-grid pcb interconnects

## Slide 21: Electrical Schematic – ESP pcb
ESP-grid cabling

## Slide 22: Electrical Schematic – ESP pcb
peripheral connectors

## Slide 23: Electrical Schematic – ESP pcb
Battery isolation switch

## Slide 24: Electrical Schematic – ESP pcb
Esp 32

## Slide 25: Electrical Schematic – ESP pcb
Motor

## Slide 26: Electrical Schematic – ESP pcb
Speaker

## Slide 27: Electrical Schematic – ESP pcb
Input multiplexer

## Slide 28: Electrical Schematic – ESP pcb
power regulation

## Slide 29: Electrical Schematic – ESP pcb
Battery charger

## Slide 30: Electrical Schematic – ESP pcb
Serial programmer

## Slide 31: PCB Layout – Grid PCB
Overview
Dimensions
  85.555mm x 79.616mm
  3.368in x 3.134in
Features
  Input Selection Mux
  Boat Input and LED Nodes
  Connectors

## Slide 32: PCB Layout – Grid PCB
Input Selection Mux

## Slide 33: PCB Layout – Grid PCB
Boat Input and LED Nodes

## Slide 34: PCB Layout – Grid PCB
Connectors

## Slide 35: PCB Layout – ESP PCB
Overview
Dimensions
  85.555mm x 79.616mm
  3.368in x 3.134in
Features
  ESP32
  ESP32 to Grid Connectors
  Peripheral Connectors
  Motor
  Speaker
  Input Multiplexer
  Power Regulation
  Battery Charger
  Battery Isolation Switch
  Serial Programmer

## Slide 36: PCB Layout – ESP PCB
Overview - Render
Dimensions
  85.555mm x 79.616mm
  3.368in x 3.134in
Features
  ESP32
  ESP32 to Grid Connectors
  Peripheral Connectors
  Motor
  Speaker
  Input Multiplexer
  Power Regulation
  Battery Charger
  Battery Isolation Switch
  Serial Programmer

## Slide 37: PCB Layout – ESP PCB
ESP32

## Slide 38: PCB Layout – ESP PCB
ESP TO GRID INTERCONNECTS

## Slide 39: PCB Layout – ESP PCB
PERIPHERAL CONNECTORS

## Slide 40: PCB Layout – ESP PCB
MOTOR

## Slide 41: PCB Layout – ESP PCB
SPEAKER

## Slide 42: PCB Layout – ESP PCB
INPUT MULTIPLEXER

## Slide 43: PCB Layout – ESP PCB
POWER REGULATION

## Slide 44: PCB Layout – ESP PCB
BATTERY CHARGER

## Slide 45: PCB Layout – ESP PCB
BATTERY ISOLATION SWITCH

## Slide 46: PCB Layout – ESP PCB
SERIAL PROGRAMMER

## Slide 47: PCB Layout
Power Considerations
Schematic Subsystem | Maximum Current | Maximum Trace Length | Calculated Trace
ESP32 | 1,100 mA | 10.5 in | 17.5 mils
LEDs (per Grid PCB) | 120 mA | 11.002 in | 14.5
LEDs (total) | 1,920 mA | 8.7 in | 37.8 mils
LCD | 40 mA | 2.7 in | 0.181 mils
Speaker | 460 mA | 2.7 in | 5.27 mils
USB to Serial | 500 mA | 5.9 in | 5.91 mils
Lipo Charger | 550 mA | 5.9 in | 6.74 mils
Motor | 260 mA | 5.89 in | 2.4 mils
3.3V to ESP, Speaker, LCD | 2,420 mA | 10.1 in | 52 mils
5.5V Power Line | 1,310 mA | 6.1 in | 22.3 mils

## Slide 48: Prototype progress
Circuits Prototyped
Keypad Detection (Complete)
SPI Communication to LCD Board (Complete)
Multiplexer Array Scan (Complete)
Pull-Up Resistor Boat Detection (Complete)
Rumble Motor (Complete)
Speaker Output (In-Progress)
LED Array (Complete)
Power System (Not Started)

## Slide 49: Prototype progress
Microcontroller
ESP32
Speaker
LCD
Button Matrix
4x4
Rumble Motor
Ship Slot 0
8x1
Mux0
8x1
Mux7
8x1
Mux
LED Daisy Chain 1
LED Daisy Chain 128
…
Backup
Battery
DCDC Converter
Ship Slot 63
…
8
8
8
1
1
SPI
(no MISO)
3
8
3
3
…
USB
USB to UART
Charger
2
4
2
1
1
2
2
2
Game Server
User
Device
Completion Status
Hardware Only
Firmware &
Hardware
Not Started
DAC

## Slide 50: Software development status
Embedded Software Server and API
Keypad Scanning (Complete)
SPI Communication (Complete)
Boat Slot Scanning through Multiplexers (Complete)
Boat Slot Identifying (Complete)
Rumble Motor (In-Progress)
Speaker playing (In-Progress)
Manage Gameflow (Not started)
Parse and send data through Websocket (Not started)
Organize code into full system (Not Started)
LED Array (Complete)
Initialize Websocket Connection (Complete)
Account/DB Requests (In-Progress)
Game AI (Not Started)
Web Game Interface (Not Started)
Create User Account (Complete)
Link MCU Device to Account (Complete)
General Game Flow (Complete)
Friend Requests (Complete)

## Slide 51: software development status
server account
Jest game flow test cases

## Slide 52: Project Timeline
Starting from Midterm Design Review
Task | Week 9 10/18 - 10/22 | Week 10 10/25 - 10/29 | Week 11 11/1 - 11/5 | Week 12 11/8 - 11/12 | Week 13 11/15 - 11/19 | Week 14 11/22 - 11/26 | Week 15 11/29 - 12/3
PCB's Ordered |  |  |  |  |  |  | 
Circuit Prototyping | Speaker & Power | Speaker & Power | Speaker & Power |  |  |  | 
Embedded Software Development | Speaker & Motor | Speaker & Motor | Organize Code | Organize code | LED Array |  | 
Server Software Development | Web Game Interface | Web Game Interface | Game AI | Game AI | Testing with Physical device |  | 
MCU to Server Gameflow communication |  | Finish all MCU to server packets | Receive & parse data from server | Use as full game flow operation | Debugging & testing |  | 
PCB Arrival |  |  |  |  |  |  | 
Order 2nd Board Materials |  | Any Additional | Materials upon | PCB Arrival |  |  | 
1st Board Construction |  |  | Soldering | Soldering & Placement | Full Assembly |  | 
2nd Board Construction |  |  |  |  | Soldering & Placement | Full Assembly | 
Hardware/ Software debugged & implemented |  |  |  | Implement & debug on Board 1 | Implement & debug on Board 1 | Implement & debug on board 2 | Implement & debug on both boards
Testing |  |  |  |  |  |  | 

## Slide 53: 3D Printing
Questions?